## Slide 1: DIALYSIS ADEQUACY
Hafez Bazaraa

## Slide 2: Case #1
M.H. is 6 y old (16Kg) on regular HD.
Predialysis serum creatinine is 5mg/dL, Urea 80 mg/dL, Bicarbonate 21 mmol/L, Hb 8
and postdialysis urea 35 mg/dL.
The father is insisting the child is now better and it is in his best interest to shorten dialysis from 4 to 3 hrs.
Do you agree?

## Slide 3
Whenever dialysis is indicated,
the patient should receive ADEQUATE DIALYSIS
How would you define, based on
intent of REPLACING RENAL FUNCTIONS?

## Slide 4: The start ….
Kolff, a Dutch physician constructed the first working dialyzer in 1943 during the Nazi occupation of the Netherlands
Using sausage casings, beverage cans, a washing machine, and other items
16 patients with ARF unsuccessfully treated
In 1945, a 67-year-old comatose woman regained consciousness following 11 hours of HD and lived 7 yrs before dying from an unrelated condition.

## Slide 5: The start …
A desperate attempt to rescue
VA largely acute non-renewable; using intra-arterial rigid devices
The kidney has been the first solid organ whose function was approximated by a synthetic device
And is so far the ONLY for long-term replacement

## Slide 6
Whenever dialysis is indicated,
the patient should receive ADEQUATE DIALYSIS for
GOAL
Survival
Minimizing morbidity
Quality of life
Given the effect of dialysis itself on these !!!

## Slide 7
What constitutes adequate dialysis?
Can we measure dialysis?

## Slide 8
What constitutes adequate dialysis?
Can we measure dialysis?
Measurements related to native KF
  Urea and creatinine
  Common, yet far from ideal !!!
  Clearance
  Extent of removal independent of level

## Slide 9
Frank Gotch introduced the concept of adequacy of dialysis
when he proposed the ‘Urea Clearance’ concept
as a measure of dialysis efficacy

## Slide 10: KT/V: HD Clearance Concept
KT/V (urea) is the fractional urea clearance per session
KT= volume of blood cleared during session
V= total volume of distribution of urea (=TBW)
UREA: easily diffusible, easily measurable, evenly distributed over TBW

## Slide 11: The ‘very’ basic concept
Blood passing through the dialyser is cleared
So blood flow x time is the amount cleared
KT/V =1 is when that volume equals patient TBW
10 Kg; V=6000 mL
Cl 50 mL/min x 120 min = 6000 mL; KT/V=1

## Slide 12: The ‘very’ basic concept
Plasma solute concentration decreases fairly rapidly during dialysis
Because dialysed blood is returned to patient !!!
So KT/V of 1.00 removes only 63% of solute
ISSUE#1/2

## Slide 13: The ‘very’ basic concept
Post-dialyser urea is very low BUT NOT ZERO
So NOT ALL blood flowing is cleared
K ≠ flow, but depends also on
  Dialyser size & clearance (KoA)
  Blood flow relative to dialyser size
  Dialysate flow
ISSUE#2/2

## Slide 14: How KT/V is calculated
From URR
KT/v= -In(1-URR)

## Slide 15: How KT/V is calculated
From URR
KT/v= -In(1-URR)
Corrected for uF & Urea generation
Daugirdas (1995) natural logarithm formula
KT/v= -In(R-0.008xt)+(4-3.5xR)x0.55UF/V
Where R=1-URR or post/pre urea
The machine can do it !!!!

## Slide 16: The 2-pool Kt/V model Urea is more rapidly removed from ECF

## Slide 17: The 2-pool Kt/V model Urea is more rapidly removed from ECF

## Slide 18: The 2-pool Kt/V model Urea is more rapidly removed from ECF
Immediate post-dialysis urea overestimates KT/V by apx 0.2
Equilibrated KT/V:
Obtain post sample 1 hr after dialysis ?
Use correction formula
NB A-V gradient for urea occurs during Dx when using AV access where arterial blood has lower conc up to 2 min post Dx

## Slide 19: KT/V TARGETS
1.2 is the minimum acceptable
1.4 is the desirable target
Based on Sp KT/V and 3x/wk schedule

## Slide 20: Case #1
M.H. is 6 y old (16Kg) on regular HD.
Predialysis serum creatinine is 5mg/dL, Urea 80 mg/dL, Bicarbonate 21 mmol/L, Hb 8
and postdialysis urea 35 mg/dL.
The father is insisting the child is now better and it is in his best interest to shorten dialysis from 4 to 3 hrs.
Do you agree?

## Slide 21: Case #1
On a 4 hr session:
- He has a URR 56%, uF 1000mL

## Slide 22: Case #1
On a 4 hr session:
- He has a URR 56%, uF 1000mL, KT/V of 1.0
- He is underweight and wasted
- He has poorly controlled anemia
He is asking for reducing session time
Do you agree?

## Slide 23: PD ??
In nephrology, adequacy first used to describe an appropriate dose of HD
Adequacy for peritoneal dialysis adopted later
Conceptual overall goal equivalent to HD,
calculations not equivalent
Quite similar to native renal clearance calculations

## Slide 24: PD
Renal clearance: UxV/P
Or Urine urea conc x Urine volume / plasma urea concentration

## Slide 25: PD
Renal clearance: UxV/P
Or Urine urea conc x Urine volume / plasma urea concentration
Dialysis clearance: DxV/P
Or D/P ratio x Dialysate drain volume

## Slide 26: PD: weekly KT/V
D/P ratio (urea)
X Dialysate volume per day = K
X 7 days =KT / TBW = KT/V
Add native kidney clearance
Minimally acceptable: 1.7-1.8
Desirable target: 2.0
+ Weekly creatinine clearnce 50L/ 1.73m2 ?

## Slide 27: PD: PET
Measurement of equilibration (D/P ratios) of solutes
To assess membrane function (blood/ dialysate transport)
Steps:
  Drain to dryness
  Standard fill (2L or 40 mL/Kg, 2.27% glucose)
  Sample dialysate at 0,2,4hrs, & plasma (assumed constant)

## Slide 28
UF correlates with 4-hr D glucose and negatively with D/P creatinine

## Slide 29: Values of PET
Peritoneal membrane transport classification
Predict dialysis dose
Choose peritoneal dialysis regime
Monitor peritoneal membrane function
Diagnose acute membrane injury
Diagnose causes of inadequate ultrafiltration
Diagnose causes of inadequate solute clearance
Estimate D/P ratio of a solute at a particular time

## Slide 30: A very restrictive summary
Do PET & clearance after 6w, repeat clearance q6Mo:
Transport is related to target dwell time (high=fast)
Dialysis dose shall depend on dialysate volume when time is optimum
Consider volume tolerance (vs ++runs)

## Slide 31: Case #2 IS THAT OK?
A.S. is two yrs old, 10 Kg weight on CAPD with 4 exchanges per day of 400 mL each. She is still passing urine & has the following lab results:
Blood Urea 90mg/dL Creatinine 4mg/dL
Dialysate drained 1800mL
Dialysate Urea 80mg/dL Creatinine 3mg/dL
Urine volume 200mL
Urine Urea 100mg/dL Creatinine 8mg/dL

## Slide 32: Case #2 IS THAT OK?
10 Kg  V=6000 mL
D/P Urea= 80/90
K= 80/90X1800=1600mL/day
Weekly KT=1600X7=11200mL

## Slide 33: Case #2 IS THAT OK?
10 Kg  V=6000 mL
D/P Urea= 80/90
K= 80/90X1800=1600mL/day
Weekly KT=1600X7=11200mL
Urine urea Cl =100X200/90=222mL/day
=1554mL/wk
Total KT=12754mL
Weekly KT/V=2.13 OK

## Slide 34: Case #2 CREAT?
10 Kg  V=6000 mL
D/P Crea= 3/4  K= 3/4X1800=1350mL/day
Weekly Cl=1350X7= 9450mL
Urine crea clearance=8X200/4=400mL/day
=2800mL/wk
CCl=12.25 L/wk
BSA= 0.47  CCl= 45L/wk/1.73m2

## Slide 35: ADEQUATE DIALYSIS?
KT/v is based on urea (Mwt 60)
Adequate fluid control
MMwt clearance (role of convection)
Minimization of dialysis- associated morbidities

## Slide 36: Fluid control: dry weight
The goal is to render pt euvolemic
With intermittent fluid removal on HD, tolerance of extra fluid removal becomes an issue (uF vs refill)
Was defined as the lowest post Dx weight a patient can tolerate without the development of symptoms or hypotension !!
Henderson LW; 1980

## Slide 38
No (<5%) change in bl vol  more to remove
Rapid/ excessive drop  too rapid uF
Progressive decline (max 8% 1st hr, 4%/h, 16% total)  OK
+ve refill  more to remove
BVM

## Slide 39: Fluid control: assessment
Clinical
Evidence of overload (HTN, oedema, ..)
Silent (subclinical) overload
Dialytic hypotensive episodes
Dehydration, hypovolemia
Supplemental tools
CVP, IVC, Bioimpedance, BVM
Change: ++ dry wt with Growth, with ++ in muscle/fat with ↓ uremia

## Slide 40: ACUTE CRITICAL CASES
Fluid control may be the most important indication/ target
Correction of electrolyte-acid/base also required
MMWT (eg cytokines) clearance could help
High small MWT clearance is important in hypercatabolic patients
Hemodynamic instability commonly a concern
Achieving KT/V recommended for chronic dialysis has little relevance in critically ill patients

## Slide 41: ACUTE DIALYSIS: The options
Acute P.D.
Conventional acute H.D.
SLED
CRRT

## Slide 42
 | APD | AHD | SLED | CRRT
Solute Clearance | ++ | ++++ | +++ | + CVVH ++ HDF
MMWT Clearance | Variable | Minimal except oHDF |  | Yes α HF volume
Fluid Removal | Variable | Rapid | Slow | Slow
Control of outcomes | + | ++ | ++ | ++
Physio-logical? | ++ | + | ++ | +++
Cost & difficulty | Minimal | Mod | As HD + longer | High

## Slide 43: Case#3
N.M., a 10-yr old (20 Kg) boy first presented with bilateral atrophic kidneys
Serum creatinine 13mg/dL, urea 280mg/dL, K 7mmol/L, pH 7.1, HCO3 6mmol/L
He will be dialyzed using a blood flow of 100ml/min on a dialyser with urea clearance of 80ml/min for that flow
How long should the first dialysis session be given that he is estimated to need to remove 1000 mL of fluid during dialysis?

## Slide 44: First dialysis & disequilibrium
Target urea reduction 30%-40%
Mostly equals KT/V of 0.4-0.5
Knowing V (=TBW) and K (dialyzer and blood flow), calculate session time

## Slide 45: Case#3
V= 20x 0.6 = 12 L
K= 80 mL/min
For KT/V= 0.4
80x T / 12000 = 0.4
T= 60 min.
But UF should take longer !!!

## Slide 46: Adequacy is a concept, not just a number
In a narrow sense, adequate small MWT solute clearance
More broadly
  Fluid status - Acid-base
  Mineral metabolism
  Middle MWT
  Nutrition, anemia, growth & activity
  Long-term outcomes
How the patient feels

## Slide 48: Adequacy is a concept, not just a number
The optimum measurement of adequacy is not yet there !!!
Use available measurements
and Consider the patients’ overall condition

## Slide 49
T
H
A
N
K
Y
O
U